## Slide 1: Computer Architecture (x86-64)
Devin A. Matthews
UT Austin
MolSSI Software Summer School 2017

## Slide 2: Computing isn’t like your Gran^H^H^H^H Advisor Remembers it…
Computers have gotten faster (more GHz), but they’ve also changed and developed on a fundamental level
  Example: a Cray-YMP (1988) could deliver near-peak speed when streaming from memory
  A multi-core Broadwell Xeon can only deliver about 1% of peak performance from memory
New features make old optimization strategies obsolete:
  Out-of-order execution
  Superscalar execution
  Vectorization (aka SIMD, not to be confused with vector machines!)
  Multiple levels of cache
  Multi-core
  Many-core
  Multi-socket
  Distributed computing
  And so on…
Compilers (and languages) have gotten better too, but they aren’t magic. To get the best performance, you have to be aware of what the computer is actually doing.

## Slide 3: Why is fast code important?
Writing fast code takes time and effort, but when done right it saves a lot more time than you put in.
Computer time costs $$ and grant-writing time. Why not use it effectively?
Fast code allows new and bigger simulations. Sometimes this leads to being able to do fundamentally new science.
Execution time savings are multiplied by number of users and number of times run. So write code that can be reused and shared. Corollary: don’t write it if someone else already has.

## Slide 4: So what’s in a modern computer?
SATA
USB
etc.
PCI-e

## Slide 5: A simple model:
Instructions
Data
Data

## Slide 6: Instructions vs. data
Harvard Architecture:
Von Neumann Architecture:
Instructions
Data
Most Modern Architectures:
Instruction cache
Data cache
Instructions and Data
Instructions and Data
Unified cache

## Slide 7: Instruction examples
Math
Logic
Memory
Flow control
ADD SUB MUL DIV SHL/SHR/SAR
VADDPD VFMA231SD VSQRTSD VRCP28PS
TEST CMP SETxx CMOVxx AND/OR/XOR/…
MOV LEA PREFETCH VMOVUPS VBROADCASTSS
CALL/RET JMP Jxx REP/REPxx
(xx = AE, NZ, GE, etc.)

## Slide 8: Instruction latency and throughput
Latency is how long it will take in cycles for the results of the instruction to be ready. Lower is better.
(Reciprocal) Throughput is how many cycles on average do you have to wait between two instructions of the same type. This can be lower than the latency because of pipelining and superscalar execution. This is also called CPI (the inverse of IPC). Lower is better.
VMULPD
VDIVPD

## Slide 9: Superscalar execution
Modern processor break instructions down in smaller pieces called µops.
The rate at which instructions can be completed is limited by 1) instruction fetch and decode, and 2) availability of execution ports for the resulting µops.
Instruction Fetcher
Instruction Decoder
Scheduler and Queue
(~50-100 entries)
~16B/cycle
~5-6 µops/cycle

## Slide 10: Out-of-order execution
Instruction Fetcher
Instruction Decoder
Scheduler and Queue
(~50-100 entries)
~16B/cycle
~5-6 µops/cycle
If the processor needs to wait for data to arrive, it can execute other instructions in the mean time. This is only possible when the instructions do not have a data dependency, i.e. the output of one is an input of another.
Reorder Buffer (~200 entries)
Load Buffer
Store Buffer

## Slide 11: Pipelining
In addition to executing multiple instructions at a time in different executions units, the same execution unit can execute multiple instructions through pipelining. This is especially important for +, -, and * operations of floating point data (but not /!).
Note that pipelining also exists in the interaction of instruction fetching, decoding, and µop scheduling: these all run at the same time on different instructions.
ADD
1
ADD
2
ADD
3
ADD
4
Time

## Slide 12: Branches
All kinds of flow control get converted into branch instructions (or jumps). The processor has to decide which branch is more likely so that it can continue to prefetch instructions and execute out-of-order. If the processor guesses wrong, you pay a branch misprediction penalty (~15-20 cycles).
Processors have gotten pretty good at predicting branches, including pattern recognition for nested loops, but reducing the number of branches can still help.

## Slide 13: Single Instruction Multiple Data (SIMD)
Basically all processors for the past 10 years can operate on vectors of floating point and (more recently) integer numbers:
  MMX, 3dNow!: legacy SIMD extensions (90’s)
  SSE2-SSE4.2: 2x double or 4x float (2000’s)
  AVX: 4x double or 8x float (2010’s)
  AVX2: same as AVX but adds integer support and FMA
  AVX512: 8x double or 16x float (2016)
    Currently on KNL, just released for Xeon.
vaddpd ymm2, ymm1, ymm0
vbroadcastss ymm0, [rax]
vfmadd213pd ymm0, ymm1, [rcx]
⊕ ⊕ ⊕ ⊕
⊗ ⊗ ⊗ ⊗
⊕ ⊕ ⊕ ⊕
ymm0
ymm1
ymm2
ymm0
ymm1
memory at [rcx]
ymm0
memory
at [rax]

## Slide 14: The memory hierarchy
Memory Level | Size | Latency | Bandwidth | Technologies
Registers | ~5K, 624B visible | n/a | n/a | SRAM/DFF
L1 cache | 32K | ~5 cycles | 64B read 32B write per cycle | SRAM
L2 cache | 256K-1M | ~15 cycles | 64B per cycle | SRAM
L3 cache | ~1M-50M | ~20-30 cycles | 32B per cycle | SRAM
Memory | GBs | ~100 cycles | ~100GB/s (<10B per cycle) | DRAM
Network (remote DMA) | PBs | 1000s of cycles | 1-10GB/s | Ethernet, Infiniband, Custom
Disk (SSD) | TBs | >100,000 cycles | ~1GB/s | Flash memory, PCIe or SATA
Shared L3 Cache
Interconnect

## Slide 15: Registers
x86-64 processors have 16 64-bit integer registers and 16 128-bit vector registers.
AVX extends the vector registers to 256 bits.
AVX512 increases this to 32 512-bit vector registers.
Most inputs and outputs of instructions must be registers. Some instructions allow one memory operand.
The “name” of each register is not important to the compiler. Register renaming allows the processor to use different physical registers for instructions that use the same register name.
Since the number of physical registers is much larger than the number of names (~10x), this avoids many false data dependencies.

## Slide 16: Cache
The level 1, 2, and 3 caches are all accessed in units of (generally) 64B, called a cache line.
If the entire cache line is not used, bandwidth can be wasted.
When the caches become full, cache lines are evicted based on some policy such as least-recently used (LRU).
If a piece of data is used again, it can be accessed using non-temporal loads and stores, to keep from evicting other data.
Cache lines be proactively moved to one of the caches by a prefetch instruction. The processor also does hardware prefetching based on observed usage patterns.
A given entry in the cache can only store cache lines from certain memory locations. This is referred to as cache associativity. One ramification of this is that repeated accesses to data at intervals of large powers of 2 in bytes (2n ≥ 4KB) reduces effective the cache size drastically.

## Slide 17: Virtual memory
The memory of a program is divided into pages, generally of size 4KB.
The pages are mapped by the hardware and operating system onto the physical memory.
Since the location of data doesn’t match the underlying hardware, this is called virtual memory.
The mapping from virtual to physical memory is cached in the TLB, but only for a limited number of pages.
Accessing a page that does not have its mapping cached causes a TLB miss. This generally costs O(100) cycles.
If the page has not been assigned a physical address (e.g. if it hasn’t been accessed before), then a page fault occurs, costing an additional O(1000) cycles.

## Slide 18: Summary so far
The processor can do lots of things at once:
  Execute out-of-order
  Execute multiple instructions (superscalar)
  Pipeline sequences of instructions
  Predict branches and speculatively execute
  Calculate multiple results simultaneously with SIMD
The bottleneck is getting data from memory (or beyond)
  (Almost) all data has to be brought into registers before being used.
  Caches hold a small amount of data closer to the processor
  Cache lines and cache associativity make some access patterns more efficient
  Virtual memory paging can cause additional delays